## Slide 1: Advancing Biofuel Production with Pyrolysis and Gasification – Integrating the benefits of Carbon Capture and Hydrogen Production
BioTheRoS Online Webinar, 12th May 2026
Moderation: Andrea Sonnleitner (BEST)
Speakers: Patrick Reumerman (BTG), Doris Matschegg (BEST), Philipp Graefe (BEST)
The BioTheRoS Project has received funding from the European Union’s Horizon Europe research and innovation programme under Grant Agreement No. 101122212.

## Slide 3: BioTheRoS General Presentation: Gasification and pyrolysis technical overview
Patrick Reumerman, BTG

## Slide 4: BioTheRoS Overview
4
BioTheRoS is an EU Horizon Programme under Grant Agreement No 101122212 running from 2023
Project Details
Consortium Members
Demonstration Cases
Application in pyrolysis and upgrading units in Netherlands & gasification unit in Austria

## Slide 5: BioTheRoS Objectives
BioTheRoS develops innovative & cost-competitive Fast Pyrolysis-to-biofuels and Gasification-FT-Synthesis value chains, combining Carbon Capture Utilization (CCU) and fuel upgrading for accelerating the scale-up of sustainable biofuels.
BioTheRoS Goal: Transfer biomass into an opportunity
1.
Development of cost-effective & sustainable technologies for thermochemical conversion of biomass to produce biofuels to TRL5
2.
Selection and assessment of several biomass feedstocks suitable for scaled-up sustainable pyrolysis & gasification biofuel value chains employing predictive biomass demand AI models
3.
Development of scale-up rules of biofuels production based on advanced modelling techniques and lab/pilot-scale trials.
Development of an LCSA framework, integrating technical, environmental, economic & social parameters via multi-criteria decision analysis techniques
4.
5.
Identification of concrete measures to improve the sustainability of thermochemical conversion of biomass to biofuels via pyrolysis and gasification
6.
Provide clarity into the market dynamics of scaled-up pyrolysis and gasification biofuel value chains
23/10/2025

## Slide 6: Demo sites & related technologies
23/10/2025
The Netherlands – Pyrolysis and Upgrading units
Pyrolysis Units:
Bench-scale unit: 2–5 kg/h
Pilot plant: 80–200 kg/h
Upgrading Unit (for pyrolysis oil to fuels):
Continuous operation
Capacity: 0.8–1.5 kg/day
Austria – Gasification Unit
Gasification Units:
  1 MW DFB reactor: ~200 kg/h feed rate
  250 kW Fischer–Tropsch pilot unit: produces 15-20 L of FT raw product
Upgrading Unit (for FT waxes to fuels):
  Hydrocracking pilot plant located in Greece

## Slide 7: Gasification – transport fuels value chain
Wood chips
Gas production
Synthesis
Gas cleaning
Fine gas cleaning
FT-synthesis
Full Gasification value chain operation
Gasifier
Forestry residue
FT raw product
  The full value chain was succesfully demonstrated.

## Slide 8: Gasification – Dual fluidised Bed technology
Chart: 
 | 41
 | 24
 | 23
 | 10
 | 2
C2H4
CH4
CO2
CO
H2
2%
  Separation gasification and combustion means no nitrogen in syngas, and a very high quality (high H2 content)

## Slide 9: Fast Pyrolysis Value Chain
Fast Pyrolysis
Hydrotreatment
Distillation
Biomass
Advanced biofuels
FPBO
HPO
Biomass
Organic Vapour
Oil
Condensor
T ~ 20 – 50 °C
Fast
Pyrolysis
Reactor
T ~ 500°C
Pyrolysis Oil
Char
Combustor
T ~ 550°C
Air
Flue Gas
Ash
Sand & char
Sand
Fuel gas
Water content
Density
LHV
Acid Number
Sulfur
FlashPoint
Cetane Number
MCRT
wt%
kg/m3
MJ/kg
mgKOH/g
wt%
°C
-
wt%
25
1,170
16
70
< 0.05
?
< 20
> 15
  Simplified representation of BTG’s pyrolysis process

## Slide 10: FPBO to advanced biofuels
SPO
SDPO
HPO
SPO = Stabilized Pyrolysis SDPO = Stabilized Deoxygenated Pyrolysis Oil HPO = Hydrotreated Pyrolysis Oil

## Slide 11: Integration of CC and H2 technologies
HPO
Naphtha
11.9%
JET
52.3%
Marine
34.6%
  Both value chains have been successfully demonstrated on pilot scale
  Both value chains can in theory benefit from CC/H2 technologies:
CO2 can be captured for boosting gasification yields
Hydrogen is needed for the pyrolysis oil upgrading
Etc..

## Slide 12: Overview of technologies for CC(U)S
Doris Matschegg, BEST

## Slide 13: Carbon Capture Utilization and Storage CC(U)S
Carbon capture (utilization) and storage involves the capture, transport, (utilization) or long-term storage of CO2 from industrial processes.
  Since plants absorb CO2 as they grow, this is one way to remove CO2 from the atmosphere when capturing from bioenergy technologies.
The BioTheRoS project scope includes:
  technologies to capture CO2 from point sources,
  relevant for the combination with biomass gasification or pyrolysis.
   excludes DACC and pre-combustion technologies
Schematic illustration of BECCS, BECCU, CCS, CCUS, DACCU and DACCS. Source: Austrian Biomass Association

## Slide 14: BioTheRoS - CC(US) technology overview
Post combustion technologies
Membrane technologies
Cryogenics
Solid adsorption
Solvent-based absorption
Oxy-fuel combustion technologies
Chemical looping with in-situ conversion
Post-combustion
Pre-combustion
Oxy-fuel combustion
Absorption by chemical solvents
Adsorption by solid sorbents
Membrane separation
Cryogenic separation
Pressure/temperature swing adsorption
Absorption by chemical solvents
Chemical looping
Absorption by physical solvents
Chemical looping reforming
Combustion in pure oxygen

## Slide 15: Membrane separation
Membranes separate CO2 from exhaust emissions by utilizing the partial pressure difference.
These membranes are selected on two key properties:
  high selectivity (for a pure product)
  high permeability (to accommodate the high flow rate of industrial flue gas)
Membranes can be made from organic material, inorganic material or a hybrid of both.
https://bioenergyeurope.org/wp-content/uploads/2025/06/BECCS-Report_final.pdf
Benefits | Drawbacks
Low energy consumption | Fouling effect
Simple installation | Performance affected by operating conditions

## Slide 16: Cryogenics
Cryogenics uses the differences in physical properties to separate CO2.
  Boiling point in cryogenic distillation
  Desublimation properties in vapor-solid separation.
https://bioenergyeurope.org/wp-content/uploads/2025/06/BECCS-Report_final.pdf
Benefits | Drawbacks
Used commercially (for high concentration and pressure gases) | High energy demand (cooling)
Results in liquid CO2 for further use | Flow must be free of water (prevent ice formation)

## Slide 17: Solvent-based absorption
Solvent-based or chemical absorption uses a chemical solvent to absorb CO2. The solvent is regenerated by changing the temperature, which separates CO2 and solvent.
  Different chemicals have been tried to achieve the best results, aiming for:
    High absorption rate
    Large absorption capacity
    Low energy requirement for the regeneration of the solvent.
https://bioenergyeurope.org/wp-content/uploads/2025/06/BECCS-Report_final.pdf
Benefits | Drawbacks
Applied worldwide in large scale (MEA – TRL 9) | High equipment corrosion rate
New solvents are being investigated | High energy consumption
 | Environmental impacts due to solvent emissions

## Slide 18: Solid adsorption (PSA/TSA)
Solid adsorption works by adsorbing CO2 as a thin film on a solid material (e.g., zeolites, activated carbon).
  Adsorbent selection according to volume of CO2, kinetics, pore size, structure, …
By changing the pressure (PSA) or temperature (TSA) the adsorbed CO2 is released/desorbed.
https://bioenergyeurope.org/wp-content/uploads/2025/06/BECCS-Report_final.pdf
Benefits | Drawbacks
High adsorption capacity | Low CO2 selectivity
Reversible | Periodic regeneration required

## Slide 19: Chemical looping with in-situ conversion (CL-ICCC) Specific adsorption process
Oxy-fuel combustion: An air separator unit separates nitrogen from oxygen prior to combustion – fuel is combusted in an oxygen environment, instead of air.
CO2 is adsorbed at an active site of a bifunctional material and is then spilled over to the catalytic site of the bifunctional material, where it reacts with a reduction agent into valuable products such as syngas.
Benefits | Drawbacks
Potential to be efficient and comparably low-cost | In development (low TRL)
Combines CO2 capture and utilization | No retrofitting potential

## Slide 20: Overview of technologies for renewable hydrogen production
Patrick Reumerman, BTG

## Slide 21: Significance
  Both the Gasification and the Pyrolysis value chains can benefit from integration of H2 technologies
  Gasification
H2 can be necessary to obtain the right H2:CO ratio
H2 is an important component in the syngas
Pyrolysis
About 5% (wt basis) of hydrogen is needed for upgrading of pyrolysis oil to transport fuels
Boundary conditions:
Hydrogen production should be sustainable (low CO2eq emissions) because of REDII/III requirements
Technologies should be appropriate to the typical scales of gasification and pyrolysis

## Slide 22
H2 production technologies
Rapid development expected from 0.05 Mtonne/year (2024) in Europe to 14 Mtonne/y (2030) and 55 Mtonne/y (2050)
Typical technologies:
Most common (85%) of global sustainable production is SMR (Steam Methane Reforming) of Natural Gas in combination with Carbon Capture.
“Green hydrogen” can also be produced from Biowaste – though scalabilty is an issue
Electrolysis
  Low temperature electrolysis
  High temperature electrolysis

## Slide 23
Low temperature electrolysis
Based on the principle of splitting water into hydrogen and oxygen via electricity
Fully commercial (TRL 9), and being scaled up
Several types, based on the way the ions are separated:
  PEM (Membrane- separated H+)
  AME (Membrane- separated OH-)
  AWE (Electrolyte and porous diafragm)
Energetic efficiency is ca 60% - 65%
Key aspects:
  Water use and purity is an issue
  Can be switched on and off easily  direct coupling with renewable electricity production
Alkaline cell (AWE)

## Slide 24
High temperature electrolysis
Based on the principle of splitting water into hydrogen and oxygen using electricity and heat
Not yet fully commercial (TRL 8)
Carried out in Solid Oxide Electrolysis Cells. Ions migrate throug an electrolyte between 500 °C and 1000°C.
Electrical efficiency is ca 75% - 85% - rest is heat.
Key aspects:
  Water use and purity is an issue
  Promising if a ‘free’ source of high temperature heat is available
  Dynamic behaviour is more limited (‘thermal inertia’)

## Slide 25
Anaerobic Digestion and SMR
Based on the principle of reacting CH4 with water to to CO and hydrogen, using steam and a catalyst at elevated temperatures (700 – 1000°C)
Fully mature, as it is used also for hydrogen production from natural gas
The AD part – including the CO2 separation from the biogas is also fully mature.
Reasons why it is not implemented more is probably:
  Scale (max low-medium scale because of AD limits)
  High value of ‘green’ methane
Key aspects:
  Well-suited for pyrolysis upgrading because of the existence of a wastewater stream.
Air Liquide SMR plant in Anwerpen (B)

## Slide 26
Costs
Costs for hydrogen production from renewable electricity is highly dependent on geographical location – see the IEA Hydrogen production cost tracker map.
Because – in Europe – CAPEX is still a significant factor, overall H2 costs are dependent on operating hours
H2 production using SMR lower, with 3.3 Euro/kg H2, of which the natural gas component is 2.5 Euro/kg H2. This explains the attractiveness of the AD/SMR combination

## Slide 27
Summary
Hydrogen production from sustainable sources is limited – but significant scale-up is projected
Low temperature electrolysis remains a dominant technology – but with issues and specific draw-backs
Costs are highly regional, scale- and technology dependent

## Slide 28: Linking CC(U)S and hydrogen technologies with gasification
Philipp Graefe, BEST

## Slide 29: Basic DFB biomass-to-liquid process chain
Combustion reactor
Gasifi-cation reactor
Air
H2O
Impurities (particles, tars, N, S, Cl compounds)
Fischer-Tropsch synthesis
Upgrading
Chart: 
 | 41 | 24 | 23 | 10 | 3
H2
CO
CO2
10%
CH4
Rest
Product Gas
Jet and marine fuel
Syncrude
Syngas
Coarse and fine gas cleaning
Feedstock
Flue gas

## Slide 30: Basic DFB biomass-to-liquid process chain
Combustion reactor
Gasifi-cation reactor
Air
H2O
Impurities (particles, tars, N, S, Cl compounds)
Fischer-Tropsch synthesis
Upgrading
Chart: 
 | 41 | 24 | 23 | 10 | 3
H2
CO
CO2
10%
CH4
Rest
Product Gas
Jet and marine fuel
Syncrude
Syngas
Coarse and fine gas cleaning
Feedstock
Flue gas
Chart: 
 | 17 | 9 | 44 | 30
H2
9%
CO
CO2
Hydrocarbons
*FT simulation: Fresh gas H2/CO/CO2/CH4 = 41/23/24/10; Xpp=65%, Recycle = 50%, SCO2=5%, SCH4=7%
FT tail gas composition*

## Slide 31: Integration of CO2 separation and utilization
Combustion reactor
Gasifi-cation reactor
Air
H2O
Impurities (particles, tars, N, S, Cl compounds)
Fischer-Tropsch synthesis
Upgrading
Chart: 
 | 19 | 31 | 35 | 7 | 8
H2
CO
CO2
CH4
Rest
7%
Product Gas#
Jet and marine fuel
Syncrude
Syngas
CO2 recycling as gasification agent
CO2 recycling as gasification agent
Chart: 
 | 27 | 14 | 15 | 38
H2
14%
CO
CO2
Hydrocarbons
15%
*FT simulation: Fresh gas H2/CO/CO2/CH4 = 41/23/5/10; Xpp=65%, Recycle = 50%, SCO2=5%, SCH4=7%
#Examplary gas composition with CO2 as gasification medium
FT tail gas composition*
Coarse and fine gas cleaning
Feedstock
Flue gas

## Slide 32: Integration of Tail gas valorization
Combustion reactor
Gasifi-cation reactor
Air
H2O
Impurities (particles, tars, N, S, Cl compounds)
Fischer-Tropsch synthesis
Upgrading
Chart: 
 | 19 | 31 | 35 | 7 | 8
H2
CO
CO2
7%
CH4
Rest
Product Gas#
Jet and marine fuel
Syncrude
Syngas
Tail gas (reforming)
CO2 recycling as gasification agent
CO2 recycling as gasification agent
Chart: 
 | 44 | 23 | 24 | 9
H2
CO
CO2
Hydrocarbons
9%
*FT simulation: Fresh gas H2/CO/CO2/CH4 = 41/23/5/0; Xpp=65%, Recycle = 50%, SCO2=5%, SCH4=7%
#Examplary gas composition with CO2 as gasification medium
FT tail gas composition*
Coarse and fine gas cleaning
Feedstock
Flue gas

## Slide 33: Integration of H2 addition
Combustion reactor
Gasifi-cation reactor
Air
H2O
Impurities (particles, tars, N, S, Cl compounds)
Fischer-Tropsch synthesis
Upgrading
Chart: 
 | 19 | 31 | 35 | 7 | 8
H2
CO
CO2
7%
CH4
Rest
Product Gas#
Jet and marine fuel
Syncrude
Syngas
Tail gas (reforming)
CO2 recycling as gasification agent
CO2 recycling as gasification agent
Chart: 
 | 58 | 29 | 9 | 4
H2
CO
CO2
Hydrocarbons
4%
*FT simulation: Fresh gas H2/CO/CO2/CH4 = 66/33/1/0; Xpp=65%, Recycle = 50%, SCO2=5%, SCH4=7%
#Examplary gas composition with CO2 as gasification medium
FT tail gas composition*
Coarse and fine gas cleaning
Feedstock
Flue gas
H2
H2 to valorize additional CO2 and provide energy
H2 for hydroprocessing
H2 make-up for excess CO

## Slide 36: Linking CC(U)S and hydrogen technologies with pyrolysis
Patrick Reumerman, BTG

## Slide 37: Pyrolysis value chain
Feedstock
Pyrolysis
FPBO
Stabilisation and hydrotreatment
HPO
Distillation
Naphtha
Bio-jet
Biodiesel
Steam, electricity
Air
Flue gas
N2
Purge
C1-C4
Wastewater
H2

## Slide 38
Feedstock
Pyrolysis
FPBO
Stabilisation and hydrotreatment
HPO
Distillation
Naphtha
Bio-jet
Biodiesel
Steam, electricity
Air
Flue gas
CO2
Purge
C1-C4
CO2
CCU
  Flue gas CO2 can be captured for external use – and as purge gas
H2
Wastewater

## Slide 39
Feedstock
Pyrolysis
FPBO
Stabilisation and hydrotreatment
HPO
Distillation
Naphtha
Bio-jet
Biodiesel
Steam, electricity
Air
Flue gas
H2
CO2
Purge
Wastewater
CO2
CCU
SMR
AD/SMR
  Hydrogen can be generated from the C1-C4 gases from distillation, and via the organics in the wastewater
C1-C4

## Slide 43: Open discussion

## Slide 45: Wrap-up and concluding remarks
Integration of CC(U)S and/or hydrogen technologies in the BioTheRoS value chains:
  Gasification
  pyrolysis
Next steps: techno-economic evaluation of integration in BioTheRoS value chains
More information, events and publications: https://www.biotheros.eu/en/home/

## Slide 46: Thanks for contributing! If you have any more comments or feedback please get in contact:
andrea.sonnleitner@best-research.eu
reumerman@btgworld.com